## Slide 1: West Berkeley Aquatic Park Stormwater Improvement Project
RICARDO SALCEDO PE, CITY OF BERKELEY – PROJECT MANAGER
December 12, 2024

## Slide 2: General Project Info
Grant funded water quality improvement project which includes the following:
  Green infrastructure adjacent to Dreamland Playground
  Trash capture infrastructure on Channing and Bancroft way east of UPRR corridor
  Storm drainage improvements along Bancroft
EPA SF Bay Water Quality Improvement Fund (SFBWQIF)
  Competitive grant program focused on improving the water quality of San Francisco Bay
  City submitted an application for funding in 2023, was selected, and Council accepted funding on June 25, 2024.
  $1.5M with a local match of $1.5M

## Slide 3: Green Infrastructure Opportunity
    Dreamland Playground adjacent to one of the City’s storm drain outfalls to Aquatic park.
    Contributing sources of pollutants:
      Illegal dumping
      Light industrial uses
      Commercial uses
      Fertilizers
    Good candidate for bioretention/flow-through planter installation.
    Attempts taken to begin incorporating green infrastructure in 2020 but limited space yielded limited treatment areas

## Slide 4: Proposed Improvements – Channing watershed

## Slide 5
Channing Watershed

## Slide 6: Bioretention/Flow-through planters
Removes pollutants from stormwater
  Filtration
  Uptake by vegetation
  Decomposing and breakdown of pollutants by microbes and fungi
Specially designed soil media
  Achieves design infiltration rate of at least 5 inches/hour
  Supports plant growth

## Slide 7: Bioretention basins
San Francisco Water Power Sewer Green Infrastructure Construction Guide Book
Typically section consists of:
  6” ponding storage above biotreatment soil
  18” Biotreatment Soil Mix
  Permeable rock layer
Overflow drainage structure can be included to direct runoff to the public storm drain system in significant storm events

## Slide 8: Flow-through planters
Unlike bioretention basins, flow-through planters do not allow infiltration into the native soil below.

## Slide 9: Project Schedule
    Construction deadline to receive Grant Funding is 2027
    Construction tentatively expected in 2026.